## Slide 1
Autonomous Shopping Cart
Innovative Retail Assistance Using AI, Robotics, and IoT
Shoubra Faculty of Engineering – Benha University
Department of Communications and Computer

## Slide 2
Paula Ayman Mikhael
OUR TEAM
Paula Emad Shohdy
Michael Samy Habashy
Muhammad Usama Aowad
Mohamed Osama Mohamed
Youssef Osman Fadel
Ebram Maher Girgis
Supervised by:
Dr. Maher Abd El Rasoul
Dr. Mohamed Rehan
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 3
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 4
Shopping shouldn’t be a challenge - it should be smart.
Retail has seen many innovations, but the shopping cart has barely changed in decades.
We present a smart, autonomous shopping cart that assists users, reduces effort, and enhances the retail experience using:
  Artificial Intelligence
  Computer Vision
  Robotics and IoT
Introduction
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 5
Manual carts are inconvenient for:
  Elderly users
  People with disabilities
  Parents managing children
Common frustrations:
  Long checkout queues
  Physical strain from pushing heavy loads
Traditional carts lack intelligence, automation, and integration with modern tech.
The Problem
Introduction
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 6
Interactive with a mobile app.
Project Objectives
Introduction
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 7
Navigates within the store using map-based SLAM.
Project Objectives
Introduction
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 8
Tracks and follows a specific user using Kinect + AI.
Project Objectives
Introduction
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 9
Recognizes products in real-time using an AI model + ESP32-CAM.
Displays recognized items and prices on the user’s phone.
Project Objectives
Introduction
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 10
System Flowchart
Introduction
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 11
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 12
Mobile Application
Objectives
User interface with cart
Show live stream from Kinect
Make user to write his ID
Show all the product in the cart
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 13
To ensure smooth performance and cross-platform compatibility, the app was built using the Flutter framework and the Dart programming language. Communication with the hardware is handled through WebSocket for the live video stream and MQTT protocol for receiving product data from the recognition system. This architecture enables efficient real-time updates with minimal latency.
  Flutter: for UI and cross-platform development.
  Dart: programming logic.
  WebSocket: for streaming live video.
  MQTT: for receiving recognized product data and sending the ID.
  Android Studio: for building and testing the application.
Technologies Used
Mobile Application
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 14
Home Screen
Mobile Application
Functionality:
Shown when the app opens.
A single button to activate and start the system.
Triggers connection to cart, sensors.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 15
Second Screen
Mobile Application
Functionality:
Shows live stream from Kinect camera.
User enters their ID in a text box.
Confirms the ID via a button.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 16
Third Screen
Mobile Application
Functionality:
Shows all items added to the cart
Calculates total price and total item count
Allows removing items from the cart
Button to navigate cart to its parking spot
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 17
Conclusion
Mobile Application
This app provides:
A modern retail experience
Reduced checkout lines
Enhanced user interaction
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 18
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 19
Ros
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 20
Ros
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 21
As ROS is sending command velocity data in
(V , W)[unicycle model]
But in real robot we need speed command for left
and right wheel
(VL,VR)
so we need some equations to convert
(V, W) to (VL,VR)
Kinematics
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 22
Kinematics
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 23
Inverse kinematics of a differential robot
odometry: is x,y and theta position of the robot according to starting location
Kinematics
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 24
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 25
Limitations of GPS in Indoor Environments
GPS accuracy (3-7 meters) is not enough for precise navigation between tight spaces.
Mapping | Technique Selection
The primary reason is that GPS signals, which operate at high frequencies, struggle to penetrate dense materials like concrete, metal, and thick walls. These obstructions scatter or weaken the signals, resulting in poor or non-existent coverage inside buildings.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 26
Our Solution
Mapping | Technique Selection
Feature | SLAM (Simultaneous Localization and Mapping) | IPS (Indoor Positioning System)
Accuracy | High (Up to 10 cm) | Varias (.5- 3 m)depends on technology (Wi-FI,BLE,UWB)
Infrastructure Required | No external setup needed | Required additional Setup (beacons).
Mapping Capability | Builds a real time map of the environment | Provides position only no mapping
Cost | Medium | Expensive
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 27
“SLAM” stands for Simultaneous Localization and Mapping. It's a technique used in robotics and computer vision to construct or update a map of an unknown environment while simultaneously keeping track of the robot's location within that environment.
SLAM problem arises when an autonomous system, such as a robot or a vehicle, needs to navigate and understand its environment in real-time.
SLAM
Mapping | Technique Selection
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 28
Gmapping, which stands for Grid-based Mapping, is a popular algorithm for performing SLAM in robotics and autonomous systems.
The Gmapping algorithm is based on particle filter and operates on laser scan data.
Definition
Mapping | GMapping Algorithm
It allows a robot to:
  Build a 2D map of an unknown environment.
  Track its position (Localization) while moving.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 29
  The robot move and collects laser scan data (from Kinect).
  It combines this with odometry (wheel encoder readings).
How It Works?
Mapping | GMapping Algorithm
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 30
It is the process of estimating a robot’s position and orientation over time motion sensors such as wheel encoders.
Odometry
Mapping | GMapping Algorithm
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 31
  Motor Encoders are sensors to the motors that measure rotation of the motor shaft.
  We use magnetic encoder.
  Encoders generate pulses as the motor shaft rotate.
  By counting this pulses these pulses, we can calculate:
  Distance traveled by the wheel.
  Speed of rotation.
  Direction(clockwise or anticlockwise).
Encoders
Mapping | GMapping Algorithm
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 32
  “Inertial Measurement Unit” IMU sensors typically consist of a combination of accelerometers, gyroscopes, and sometimes magnetometers, (IMU) sensor in robotics is to provide information about an object's orientation and motion by measuring its linear accelerations and angular velocities. This information is useful for tasks such as navigation, localization, and mapping.
  We combined wheel encoders with IMU to improve odometry accuracy. Encoders provide distance, while IMU refines orientation and detects slipping. Together, they enable more reliable localization.
Challenges
Mapping | GMapping Algorithm
Bad odometry and inaccurate localization.
Solution
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 33
  No Lidar Only Kinect.
  Convert depth image to laser scan.
Challenges
Mapping | GMapping Algorithm
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 34
  To overcome this, we used the depthimage_to_laserscan Ros package.
  It converts the Kinect’s depth data into a virtual laser scan.
Solution
Mapping | GMapping Algorithm
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 35
Simulation Scenes
Mapping | GMapping Algorithm
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 36
Practical Video
Mapping | GMapping Algorithm
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 37
Move_base
Navigation & path planning to Parking Spot
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 38
Global Planner
Navigation & path planning to Parking Spot
  Create a global path that depends on the map.
  Type of planner A* algorithm.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 39
Local Planner
Navigation & path planning to Parking Spot
  represent the immediate surroundings of the robot. It
  generating a trajectory that guides the robot from its current position to the next point on the global path. The loca planner takes into account dynamic obstacles. It operates on local costmap.
  DWA algorithm(Dynamic Window Approach)
  Set margin around the dynamic obstacles
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 40
Obstacle Avoidance
Navigation & path planning to Parking Spot
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 41
Challenge
Navigation & path planning to Parking Spot
  The Robot Stuck!
Solution
  Recovery Behavior
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 42
Practical Video
Navigation & path planning to Parking Spot
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 43
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 44
Objectives
Person Tracking
Detection: Camera detects all persons in the FOV & assign each one with a specific ID.
Select target: The target to be tracked selects his ID.
Accurate Following: Follow the target accurately through dynamic environments.
Re-Identification: Re-identify the user if they temporarily disappear.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 45
Initial Algorithm Tools
Person Tracking
YOLO: For person detection & assigning an ID to the 1st person showed in front of camera FOV.
IOU: For bounding box similarity.
Euclidean Distance (Centroid): For motion tracking.
KMeans: For Re-Identification by clustering dominant clothing color.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 46
Testing and Challenges
Person Tracking
Exit/Entry Errors
Incorrectly associated new persons entering the scene with the original target, causing tracking errors.
Occlusion Issue:
Failed to maintain tracking when the target was occluded, leading to incorrect identification of other individuals (ID swapping).
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 47
Final Algorithm Tools
Person Tracking
YOLO: For person detection & assigning a unique ID to all detected persons.
Deep SORT: (Simple Online and Realtime Tracking) is an algorithm used for multi-object tracking in video streams.
Kalman Filter: For state prediction. The state of an object typically includes its position, velocity, and acceleration. The Kalman filter predicts the state of each object in the current frame based on its last known state, accounting for the object's motion dynamics.
OSNet_ain_x1_0: Used for Re-Identification of target being tracked.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 48
Test Cases & Results
Person Tracking
Target Re-Identification with Interference
Target Leaves While a Distractor Remains
Crowded Environment and Back-Facing Target
Overall, the tracking system demonstrated high reliability, minimal identity switches, and strong re-identification performance in complex scenarios.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 49
Integration
Person Tracking
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 50
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 51
  Product Recognition is a feature that uses Computer Vision to identifies any product added to the cart by the user, saving its characteristics such as image, name, price, and quantity. These information are displayed on the Mobile Application.
  This feature includes real-time updates of the cart’s contents, whether products are added or removed.
  It allows the user to know exactly what is in their cart and which products they still need to add.
  Let’s dive deep!
Overview
Product Recognition
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 52
Previously, two open-source datasets were used for training but could not be further utilized due to the following limitations:
  Class imbalance. (Small number of images per class.)
Quality issues for some images (blur).
Products are not available in Egyptian markets
Few number of orientations per product
Grocery Store Dataset
Biscuit Wrappers Dataset
Product Recognition
Dataset
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 53
As a result, a custom dataset was made from scratch, representing 25 common consumer products found in Egyptian supermarkets and grocery stores.
Dataset
1 Beyti Full Cream Milk 900mL | 2 Bisco Misr Luxe | 3 Bisco Misr Max | 4 Bisco Misr Wafer | 5 Crystal Sunflower Oil - 800mL
6 Domty Cheese with Olive | 7 El Maleka Elbow Pasta - 400G | 8 Fa Men Anti-perspirant Roll-on | 9 Heinz Tomato Ketchup Grill | 10 Heinz Tomato Paste
11 Indomie Supermi Vegetable | 12 Knorr Vegetable Stock - 12 Cubes | 13 Lipton Yellow Label Tea Dust 40g | 14 Malh Baladna Salt - 300g | 15 Mena Foul Fava Beans
16 Nivea Soft Moisturizing Cream | 17 Oniro Teabix Biscuits | 18 Rehana Flour 1Kg | 19 Savannah Classic Soap - 125g | 20 Shepsy Salt and Vinegar Chips
21 Shepsy Tomato Chips | 22 Signal Cavity Fighter | 23 Sunshine Shredded Tuna | 24 Toledo Mushroom | 25 Zam Zam Black Eye Beans 500g
Product Recognition
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 54
Perspective
Full view, edge views, and corner views
Capturing Guidelines
Sides
Both front and back of the product
View Type
Self-standing ( without occlusion) and Handheld (with occlusion)
Product Recognition
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 55
  It comprises 25 distinct classes.
  The number of raw images captured before augmentation = 985 images.
  The number of final images captured after augmentation = 4,828 images.
Splitting ratio:
  Training set 85%: 4093 images.
  Validation set 15%: 735 images.
  Fixed random seed of 42.
Dataset
Product Recognition
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 56
Preprocessing
Product Recognition
2. Extend
Prevent out-of-boundary issues, Prevent negative coordinates during rotation, new formula was made:
1. Crop
square 1:1 aspect ratio
4.Annotate
Oriented Bounding Boxes (OBB) was used for a tighter fit, manually drawn using Roboflow’s platform
3. Resize
reduce the overall dataset size, and match the model’s required input dimensions of 640 pixels
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 57
Augmentation
Product Recognition
Rotation:
  statically by 0° (original), 90°, 180°, and 270°.
  dynamically slight rotation from -40° to +40°, however limited to 40° to prevent duplication
Shifts images horizontally and vertically by a random fraction of the image size.
Translate = 0.1
Blurring
Automatically done by Albumentations during training.
Coloring
lighting conditions can affect object appearance
  hsv_h = 0.015: Hue shifts image colors slightly.
  hsv_s = 0.3: Saturation modifies the intensity of colors img.
  hsv_v = 0.3: Value changes the brightness of the image.
Scale = 0.5
Enables models to handle objects at different distances and sizes.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 58
CV Classification phase:
First, we tried different classification only models searching for the balance between speed and highest accuracy.
using IR sensors for detection.
complicated, expensive and not an accurate event detection method (add/remove).
Classification Models | Accuracy (%)
ResNet50V2 | 94.7
ResNet101V2 | 94.4
VGG16 | 76
VGG19 | 71
Inception | 92
MobileNetV3Small | 3
MobileNetV2 | 98.7
Model
Product Recognition
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 59
CV Detection phase:
We used YOLOv8-OBB for both detection and classification.
It offered the best balance between speed and accuracy.
Training on Google Colab using Tesla T4 GPU:
  is done over 50 epochs.
  using a 640×640 image size.
  with the AdamW optimizer.
  batch size of 16.
  The final architecture comprised 144 layers.
Model
Product Recognition
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 60
Developing Visualizers:
  Webcam.
  Draw OBB, boundary line, counter.
  Trackbar.
  Log file.
Deployment
Product Recognition
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 61
  Extracted: Bounding box coordinates, confidence score, class name and tracking id.
  Smoothing Bbox through frames (webcam).
  Counting Logic:
  The product is considered added to the cart, if a product position is before the boundary and in the next frame the position is after the boundary threshold line.
  The product is considered removed to the cart, if a product position is after the boundary and in the next frame the position is before the boundary.
  Message Preparing: that includes the product ID, name, quantity (+1 or -1), and price is prepared and sent to the app.
  Error Handling: Transient detection failures using a “no_detection_counter” to reset state if no product is found. Object ID duration tracking to ignore unstable or brief detections (debouncing).
Deployment
Product Recognition
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 62
Deployment
Product Recognition
All 25 Products on Webcam
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 63
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 64
System Architecture
Wireless Communication & IoT
Arduino Mega: Low-level controller for motors via motor driver, encoders, and IMU.
Raspberry Pi 3B: Interfaces with Kinect, acts as ROS node, connects to Arduino via rosserial.
External PC with GPU: Runs ROS Master, AI models, mapping and navigation .
ESP32-CAM: Captures product video, sends to PC via WebSocket.
Mobile App: MQTT/WebSocket client for user interaction.
Access Point (Wi-Fi): Creates a local network connecting all devices together.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 65
A dedicated Wi-Fi Access Point provides a closed Local Area Network (LAN) for all devices involved in the system. This LAN ensures secure, low-latency, and internet-independent Communication between the system components.
System Network Overview
Wireless Communication & IoT
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 66
To ensure reliable identification and routing, static IPs were assigned to the PC, Raspberry Pi, and ESP32-CAM in each cart. The PC requires a static IP as it hosts the ROS Master, WebSocket server, and MQTT broker. For each autonomous cart, the Raspberry Pi and ESP32-CAM were also given fixed IPs to allow the PC to uniquely distinguish between multiple carts, and to properly route tracking, product streams, and control messages. In contrast, the mobile app connects dynamically using a DHCP-assigned IP, allowing any user device to access the system without manual configuration.
This setup ensures:
Stable routing for ROS nodes.
Easy access for any mobile device.
IP Configuration
Wireless Communication & IoT
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 67
To establish reliable and real-time Communication between the various components of the autonomous shopping cart, we used a combination of protocols, including both IoT and non-IoT standards:
  MQTT (IoT Messaging).
  WebSocket (Streaming + Event Communication).
  TCPROS (ROS native Communication).
  Bridging techniques to connect ROS with non-ROS components.
Communication Protocols Overview
Wireless Communication & IoT
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 68
Type: IoT messaging protocol (publish-subscribe).
Advantages: Efficient, Lightweight and Asynchronous messaging.
The Mosquitto MQTT broker is hosted on the PC.
  Mobile App ↔ ROS Nodes
  Start Button Sends a command to initiate and start the entire system operation.
  Parking Button Sends a parking request to the ROS navigation node to stop or return the cart.
  Person ID Input Allows the user to enter a person ID, which is sent to the tracking node to follow the selected person.
  Mobile App ↔ Product Recognition Node
  Product Table Displays product names and details received from the product recognition AI model via MQTT.
MQTT Protocol
Wireless Communication & IoT
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 69
Type: Full-duplex, persistent connection over TCP.
Advantages: Fast, real-time updates, Works well for streaming media and Compatible with browsers & mobile apps.
ESP32-CAM → PC
  ESP32-CAM acts as a WebSocket client that streams video frames to the PC WebSocket server.
  PC uses a non-ROS Product Recognition module to detect and classify items.
  PC → Mobile App
  PC streams tracking video to the app for live monitoring.
  App receives frames over WebSocket.
WEbSocket Protocol
Wireless Communication & IoT
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 70
Type: ROS-specific protocol over TCP.
Advantages: Handles publishing/subscribing between ROS nodes, Efficient within ROS architecture and Supports distributed systems.
  Registration:
  Master shares connection info (IP, Port).
  Node tells Master what topics/services it offers or needs.
  Communication:
  Nodes talk directly to each other.
  Fast real-time message passing.
TCPROS Protocol
ROS Master-Node Communication PC ↔ Raspberry Pi
Wireless Communication & IoT
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 71
The ROS Bridges are used to enable seamless Communication between ROS-based systems and external non-ROS application. Since ROS natively communicates within its own ecosystem using topics and services, it cannot directly interact with devices or services outside of ROS. This approach makes robotic systems more flexible, scalable, and accessible for broader integration.
  MQTT Bridges: To allow non-ROS mobile app to interact with ROS navigation and Person Tracking nodes.
  WebSocket Bridges: To stream video from the ROS-based Person Tracking node to the mobile app.
ROS-to-Non-ROS Communication Bridges
Wireless Communication & IoT
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 72
  Interactive mobile App
  Creating 2D map
  Navigation to parking spot
  Recognition of 25 products and they are added or removed while displaying them on the app
  Reliable tracking to individual user
Conclusion
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 73
  Using multiple cameras to do inference from different positions at the same time.
  Using LIDAR.
  Using more powerful central GPU or local jetson nano/google coral.
  Raspberry Pi Camera Module 3, 12MP.
  Payment system.
Future Work
THANK
YOU
Not just a Shopping Cart.
7
Wireless
Comm
6
Product
Recognition
5
Person
Tracking
4
Mapping &
Navigation
3
Ros &
Kinematics
2
Application
1
Introduction
CONTENT

## Slide 74
THANK
YOU